## Slide 1: A numerical modeling technique designed for error insight
Mart Borsboom
With application to 1D shallow-water flow simulations (rivers, channels, pipes, ...)
Notes: Deltares: an independent knowledge institute for applied research in the field of water and subsoil.
NB, ‘compatible’ and ‘compatibility’ are nowadays used in the numerical community to indicate (mimetic) schemes conserving certain properties at the discrete level, e.g., energy conservation. For this reason the developed discretization is now called ‘error-consistent’ (I still have to get used to that one ).
CASA Colloquium, March 18, 2020, Eindhoven University of Technology
H2I meeting, March 29 & April 12, 2021, Deltares
NSS meeting, April 22, 2021, Deltares
Kennisoverdracht Mart, July 14‒15, 2021, Deltares
Lunch lecture at VORtech, September 6, 2021, VORtech

## Slide 2: Contents
Examples of 1D shallow-water flow applications
The 1D shallow-water flow model equations
Computational model: the components
Numerical implementation: properties
Two-step numerical modeling approach
Finite volume method designed for error analysis
Test: flow over a weir (including grid adaptation)
Application: Libyan man-made river
Concluding remarks
(this presentation and other info available)

## Slide 3: 1D shallow-water flow applications

## Slide 4: 1D shallow-water equations
: channel width ( below bottom )
: free surface
: wetted cross-sectional area ( effective depth )
: hydraulic radius (± average depth), with wetted perimeter
: discharge ( average velocity )
Notes: We don’t define A (and W, P) as a function of ζ, but ζ (and W, P) as a function of A, i.e., ζ=ζ(x,A) (and W=W(x,A), P=P(x,A)) with A=A(x,t) one of the two primitive unknowns. The other one is Q=Q(x,t).  Continuity equation is linear in the unknowns and always solved exactly, because free of linearization errors.

## Slide 5: Computational model: the components
(plus user interface, grid generator, Kalman filter, …)
this presentation is about the numerical implementation
Notes: From Borsboom, “Domain Decomposition and (versus?) (Un)Structured Grids”, sep 2009 (dd&(un)struc.ppt), based on a figure taken from Borsboom, “A Finite Volume Method Designed for Error Analysis”, 1st Int. Symp. FVCA, Rouen, 1996. Note: controllers for, e.g., structures are part of conceptual model => implemented in algorithm and software, i.e., part of computational modeling.
NB, concept and nomenclature from Dee & Van Der Marel, “Validation of computer models–concepts and terminology”, WL report March 1991.
NB2, the hydrodynamic/shallow-water illustration/example of “natural system”, “conceptual model”, “algorithmic implementation” and “software implementation” taken from Mourits & Borsboom, “Flexibel, Efficiënt en Nauwkeurig Koppelen van Modellen—Taskforce Modulaire Code”, presentation DOSO meeting, December 2009.

## Slide 6: Computational model: the requirements
Computational models should be (or not) sufficiently … which is determined by the model components:
robust Phys, Num
maintainable/modular Phys, Num, Soft
realizable/analyzable/verifiable Phys, Num, Soft
flexible/generally applicable Phys, Num, Soft
extendable/improvable/reusable Phys, Num, Soft
efficient/parallelizable Phys, Num, Soft
easy to use/user friendly (e.g., virtually no options) Phys, Num, Soft
quickly available Phys, Num, Soft
relevant/fit for purpose/useful Phys, Num
accurate Phys, Num
reliable (insight in modeling errors) Phys, Num
traceable (what to do to improve results) Phys, Num
simple/understandable/teachable Phys, Num, Soft
“Too often, failure to agree with experiment is mistakenly ascribed to the turbulence model rather than inadequate numerics.” (Johnson et al., Math. Model. Nat. Phenom. 2011)
Notes: Adaptation/extension of a sheet from Borsboom, “A numerical modeling technique designed for error insight”, Sep 2021 (Borsboom_presVORtech2021.pptx, an adapted version of Borsboom_presH2INSS2021.pptx).
easy to use/user friendly  e.g., virtually no options! (especially those impossible to be specified by the non-specialist user)
ease of use/user friendliness also determined by user interface, pre-processing (including grid generation), post-processing, …
ease of analysis  elegance
From Borsboom, “A finite volume method designed for error analysis”, presentation FVCA1 1996 (Borsboom_FVmethoddesigned4erroranalysis_1stFVCA1996.pdf): … smoothness is essential for meaningful error analysis, cf. e.g. Yee, Sweby & Griffiths, JCP 1991: “… the application of the apparently straightforward numerical technique to genuinely nonlinear problems can be shown to lead to incorrect or misleading results.”
NB, sheet is similar to a shorter list in Borsboom & Van Dam, “NGHS: Application-Properties Matrices and Proofs of Concept (POCs)”, March 2012 (applpropmatrices&POCs-3_AvD-MB.ppt) where it is noted
Extendability/reusability:
numerical/software: higher efficiency (parallelization), higher accuracy, …
physical: integration with water quality, sediment, waves, …
Properties are not independent, e.g.:
different grids, different time steps  flexibility + efficiency
unstructured grids  flexibility + higher complexity (+ lower accuracy)
higher accuracy  higher complexity

## Slide 7: The basic idea
“… introduce (artificial) dissipative terms ... to give the shocks (MB: and other non-smooth features) a thickness ... somewhat larger than the spacing of the points of the network.”
“Then the difference equations may be used for the entire calculation, just as though there were no shocks (MB: and other non-smooth features) at all.”
“The quantitative influence of these terms can be made as small as one wishes by choice of a sufficiently fine mesh (MB: and a sufficiently small time step) …”
“… components whose wave-lengths are of order (MB: and whose time scales are of order ) are always falsified somewhat.”
(Von Neumann & Richtmyer, J. Appl. Phys. 1950)
(regularization à la LES)
(unified numerical implementation possible)
(basis for (automatic) grid adaptation
and time-step adaptation)
(dynamic subgrid effects can NOT be simulated!)
Notes: ABSTRACT: “The equations of hydrodynamics (MB: and the data) are modified by the inclusion of additional terms which greatly simplify the procedures needed for stepwise numerical solution of the equations in problems involving shocks (MB: and other non-smooth features).”
ABSTRACT: “The quantitative influence of these terms can be made as small as one wishes by choice of a sufficiently fine mesh for the numerical integrations.”
I. INTRODUCTION: “We describe here a method for automatic treatment of shocks (MB: and other non-smooth features) which avoids the necessity for application of any such boundary conditions (MB: supplied by Rankine-Hugoniot equations). The approximations in it can be rendered as accurate as one wishes, by suitable choice of interval sizes and other parameters occurring in the method. It treats all shocks, correctly and automatically, whenever and wherever they may arise.”
I. INTRODUCTION: “The method utilizes the well-known effect on shocks of dissipative mechanisms, such as viscosity and heat conduction. When viscosity is taken into account, for example, the shocks are seen to be smeared out, so that the mathematical surfaces of discontinuity are replaced by thin layers in which pressure, density, temperature, etc. vary rapidly but continuously. Our idea is to introduce (artificial) dissipative terms into the equations so as to give the shocks (MB: and other non-smooth features) a thickness comparable to (but preferably somewhat larger than) the spacing of the points of the network. Then the differential equations (more accurately, the corresponding difference equations) may be used for the entire calculation, just as though there were no shocks at all.”
I. INTRODUCTION: “It will be seen that for the assumed form of dissipation (and, indeed, for many others as well), the Rankine-Hugoniot equations are satisfied, provided the thickness of the shock layers is small in comparison with other physically relevant dimensions of the system.”
I. INTRODUCTION: “The method has been applied, so far, only to one-dimensional flows, but appears to be equally suited to the study of more complicated flows; …”
III. THE EXPRESSION FOR Q: “The dissipation is introduced for purely mathematical reasons.” (MB: incorrect, should be: Smoothing is introduced to keep discretization errors small compared to smoothing errors.)
VII. STABILITY OF THE DIFFERENCE EQUATIONS: “… the long-wave-length components are accurately given by (48) to (51), provided Dx and Dt are sufficiently small, but the components whose wave-lengths are of order Dx are always falsified somewhat. This falsification is harmless, provided that all physically relevant components are treated accurately; this requires not only that Dx and Dt be small (MB: enough) but also that the physically insignificant components with wave-lengths of order Dx remain small during the entire calculation. It may happen not only that the short-wave-length components are falsified but also that their amplitudes increase with increasing n (MB: n is time-step index), in spite of the stability of the differential equations. This increase is generally exponential (MB: i.e., the result of numerically unstable behavior) and, if it occurs, quickly makes gibberish of the entire calculation (MB: obviously ).”

## Slide 8: Two-step numerical modeling approach
one-step numerical
modeling
regularization step
discretization step
reduce/minimize by
means of (automatic)
grid adaptation and/or
time-step adaptation
CONCEPTUAL
MODEL
ALGORITHMIC
IMPLEMENTATION
Notes: Application of regularization is well known, cf. (I)LES.
From Borsboom, “A finite volume method designed for error analysis”, presentation FVCA1 1996: … smoothness is essential for meaningful error analysis, cf. e.g. Yee, Sweby & Griffiths, JCP 1991: “… the application of the apparently straightforward numerical technique to genuinely nonlinear problems can be shown to lead to incorrect or misleading results.”
“(This indicates that) satisfactory design criteria do not exist at the present time that would ensure captured shocks that are both narrow and free from oscillations.” … “… some form of controlled shock spreading has been the cure recommended by several investigators.” Arora and Roe, 1997
“If one can approximate functions well, one can also solve PDEs well.” Djokovic and Van Damme, 1996

## Slide 9: Difficult 1D shallow-water equations
cont.eq. and mom.eq. combined to energy equation (with ):
 take
regularization step
Easy 1D shallow-water equations
Notes: Regularization of zeta (new idea of Christmas 2022, not yet implemented):
introduce auxiliary variable zeta~
solve auxiliary regularization/smoothing equation zeta~ − d/dx(nu_zeta * dzeta~/dx) = zeta(A~), with geometry-dependent and possibly very non-smooth function zeta(A) describing how zeta depends on A, and with nu_zeta a zeta~ interpolation-error-dependent smoothing coefficient

## Slide 10: Finite volume-type collocated discretizations
finite difference-like
 ± piecewise constant
finite element-like
piecewise linear
Notes: Borsboom, “Compatibele schema’s voor stromings- en transportproblemen, de (vele!) voordelen en (slechts enkele?) nadelen”, WL memo 14 jan 1993, gepresenteerd/besproken in Thema 5 overleg van 20 jan 1993.
In Borsboom & Van Der Marel, Development of an adaptive grid procedure that compensates for discretisation errors, with an application to the 1D Burgers' equation, WL report Q1346, March 1992, no compatible discretization yet.
In Van De Langemheen, Simulation of 1-D open channel flow using a moving adaptive grid algorithm, WL report X125, November 1994, with a reference to Borsboom, M., Collected notes on: A compatible discretization and error-minimizing moving adaptive grid algorithm for one-dimensional convection-diffusion problems, July 1992--July 1994 (unpublished)
NB, in 2D piecewise (bi)linear finite element-like FV method possible on both triangles and quadrilaterals, but error analysis (cf. next slides) only possible on structured grid

## Slide 11: Error analysis
Discretization error (residual)
We have
Hence
(Borsboom, Ch.5 in Adaptive Methods of Lines, 2001)
discretization step
Notes: Error analysis must be in computational space = only space where grid spacing is constant.  Coordinate transformation x(\xi) is also a function that is to be approximated smoothly!  This takes care automatically of sufficiently smooth grids.
2nd-order accurate determination of 2nd-order discretization errors  evaluation of integrals must be at least 4th-order accurate!
NOTE: with the exception of a uniform grid, \overline{x}(\xi) is NOT equal to \hat{x}(\xi)!

## Slide 12: Equivalent 1D shallow-water-like equations
with , and with , , .
(Borsboom, Ch.5 in Adaptive Methods of Lines, 2001)
Notes: Error analysis must be in computational space = only space where grid spacing is constant.  Coordinate transformation x(\xi) is also a function that is to be approximated smoothly!  This takes care automatically of sufficiently smooth grid.
2nd-order accurate determination of 2nd-order discretization errors  evaluation of integrals must be at least 4th-order accurate!
Piecewise linear in time/Crank-Nicolson  similar piecewise linear discretization errors in time.

## Slide 13: Sub-/supercritical steady flow over a weir
100 finite volumes, uniform grid
100 finite volumes, adaptive grid
100 finite volumes, uniform and adaptive grid, solution near weir corner
100 finite volumes, uniform and adaptive grid, solution around jump
Notes: Grid size on uniform grid is 5m. Grid size on adapted grid:
at x = 0.0 largest Dx = 74.38m = 14.876 * 5m = 10^1.1725 * 5m
at x = 439.1 smallest Dx = 0.05960m = 0.01192 * 5m = 10^−1.924 * 5m
at x = 194.35 largest stretching of 0.567697 = 1/1.761503 = 10^-0.2459 = e^-0.5662
at x = 438.56 largest stretching of 0.562935 = 1/1.776404 = 10^-0.2495 = e^-0.5746
at x = 439.66 largest stretching of 1.768792 = 1/0.565358 = 10^0.2477 = e^0.5703
NB, minimization of piecewise linear interpolation errors = minimization of the leading errors in solution of discretized system of equations = minimization of the effect of residual error in numerical solution … is comparable with grid adaptation using adjoint-based error estimation

## Slide 14: Sub-/supercritical steady flow over a weir
14
100 finite volumes, adaptive grid, grid size and grid stretching
Notes: Stretching limited by implicit error smoothing/low-pass error filter with homogeneous equation (1/8−alpha)*(lambda^2+1) + (3/4+2*alpha)*lambda = 0
lambda = (alpha+3/8+sqrt(alpha+1/8)/(alpha−1/8) and lambda = (alpha+3/8−sqrt(alpha+1/8)/(alpha−1/8)=(alpha−1/8)/(alpha+3/8+sqrt(alpha+1/8).
For alpha=3 (value used in SUPSUB computations), lambda = 1.7888 and lambda = 0.55904  ln(lambda) = ±0.58154.

## Slide 15: The great man-made river
Notes: Michiel Tukker, HOPS presentation “Free surface flow in Wanda”, April 10, 2020:
“FSF water-hammer pipe was originally designed for a project in Libya, the Great Man-made River. 4000 km of pipelines, diameter 4.0 m. Deltares (then WL|Delft Hydraulics) did surge analysis and training for their engineers.”
“Keep in mind: The numerical scheme of the FSF Conduit is designed for numerical robustness and not for accuracy.”

## Slide 16: The great man-made river
4m diameter pipes through Libyan desert circular cross section approximated by dodecagon with added Preissmann slot
From presentation Michiel Tukker
Free surface flow in Wanda
April 10, 2020
Preissmann slot
Notes: Work from 1999-2000
Preissmann slot on top of pipe of approximately exponential shape: at top 0.2m wide, every next 0.05m sqrt(10) smaller, until 0.0002m=0.2m/10^3=0.2mm at distance 0.3m above top
With Preissmann slot of 0.0002m (= 0.2mm) at top (to ensure a free surface in fully filled pipes), max. wave celerity in fully filled pipe is sqrt(g*A/W) = sqrt(9.81*Pi*2^2/0.0002) = 785m/sec. This is pretty close to 1450m/sec, the speed of sound in water. NB, if relevant, the (much) lower speed of sound in water with dissolved air could be easily emulated with a slot of variable, air-concentration-dependent width.
With Preissmann slot of 0.0002m (= 0.2mm) at top, 0.220% additional storage when 110m water in slot (NB, 110m*0.2mm = 0.175% of π*2m*2m).

## Slide 17: Steady-state great man-made river
381.2km long 4m diameter pipe through Libyan desert
2000 finite volumes: 1815 of 54.96m in first 100km, 165 of 1648.8m in last 270km, 20 in between

## Slide 18: Steady-state great man-made river
2000 finite volumes, convergence history
Notes: Results from the year 2000.
Steady-state computation, hence 1/Dt_phys = 0 and theta = 1
Initial solution: Q=0m^3/sec, zeta=144m (why water level just a bit too low? Hm!)
Convergence error-dependent pseudo time step used.
High2000ultra.log: 613 iterations, 260.01sec CPUtime (in 2000) (battery-powered notebook with processor at half speed?).
Low2000ultra.log: 631 iterations, 132.15sec CPUtime (in 2000).
Estimation of convergence speed of 1D D-Flow FM for this problem is O(1,000) iterations for factor 10 residue reduction, assuming local time stepping, otherwise much slower due to variation in flow speed and in grid size. In view of its much more work per pseudo time step, SUPSUB would then be not much faster, however, in D-Flow FM nested Newton required to deal with Preissmann slot  (at least) 9 iterations per time step.
Gropp, Keyes, McInnes, Tidriri (2000), “Globalized Newton-Krylov-Schwarz algorithms and software for parallel implicit CFD”, about +- optimized pseudo time stepping and the phases during convergence: “The globalization theory of Kelley and Keyes (1998) employs a three-phase approach, but phases in practice may or may not be cleanly demarcated in residual norm convergence plots. Initially, ||u0 – u*|| ~ 1 and tau0 << 1 (MB: read CFLpseu ~ 1). During an 'induction phase', the solution is marched in a method-of-lines sense with a relatively small time step until ||u – u*|| / ||u0 – u*|| << 1. Success of this phase is governed by stability and accuracy of the integration scheme (we simply use the backward Euler method) and by the choice of initial iterate. For problems in which a complex feature, such as a shock or a flame front, must arise from a structure-free initial condition, the induction phase is typically by far the longest. (We are reminded of an observation attributed to Samarskii: 'The slower you start, the sooner you finish'.) (MB: NICE!) In a grid-sequenced problem, in which the initial iterate on a given fine grid is interpolated from a converged solution on a coarser grid and in which solution features are correctly located (if not fully resolved), the induction phase on the finest grid can be relatively brief (Smooke and Mattheij, 1979). During a second 'transition phase', the time step is built up in the neighborhood of the solution. The critical assumption is existence of a beta such that ||(I + tau f'(u))^-1|| <= (1 + beta tau)^-1 for all tau >= 0 if ||u – u*|| <= eps. Finally comes a 'polishing phase', during which the time steps approach infinity (or some user-imposed upper bound), and iterates approach the root with asymptotic Newton-like convergence. This phase is treated by a conventional local analysis, as in Kelley (1995)."

## Slide 19: Unsteady great man-made river
Comparison with measurements, low discharge
high discharge
Notes: Results from the year 2000.
Time step is 1800 sec. Anton Heinsbroek: simulations with SOBEK(-URBAN?) (version of 20 years ago?) required time steps of 1/4 sec.
Low2000ultra.logunst: average number of iterations per time step is (14659-10681)/100 – 3 extra lines = 36.78. Total CPU time: 1262.30sec (in 2000).
High2000ultra.logunst: average number of iterations per time step is (14257-10681)/100 – 3 extra lines = 32.76. Total CPU time: 1142.12sec (in 2000).
Low2000ultra_copy&uconverrorLT1E-8.logunst: average number of iterations per time step is (13494-10681)/100 – 3 extra lines = 25.13.
High2000ultra_copy&uconverrorLT1E-8.logunst: average number of iterations per time step is (13142-10681)/100 – 3 extra lines = 21.61.
Hence for low (high) discharge scenario on average 37 (33) iterations required per time step with convergence criterion of 1.E-11. With convergence criterion of 1.E-8 (in practice probably more than enough) on average 25 (22) iterations required per time step.
NB, max. CFL number based on max. wave speed 785.1m/s and smallest grid size 56.96m is nearly 26000. Max. Courant number based on max. flow speed 3.78m/sec is nearly 125.

## Slide 20: Wave run-up/run-down
9─17 iterations per time step
(12.3 on average)
 better initial solutions required to
speed up convergence per time step
Notes: Result from 2002; max.Froude number at time step 432 is nearly 18.
Largest (negative) velocity is about -7.5  Cour_max = |u_max|*Dt/Dx = 1.75
Chezy=100, domain length=40, Dx=0.4, 500 time steps, Dt=0.1, theta=0.6, convergence criterion |Dh|, |Du| < 1.E-8
_slope.log: iteration process from line 382 to line 8057, hence average number of iterations per time step is (8057-382)/500 – 3 extra lines = 12.35. Total CPU time: 17.03sec (in 2002). MB, number of iterations varies from 9-10 to 17.
2019-05-05: drying and flooding procedure used in SUPSUB consists of turning off hydrostatic pressure gradient g*h*GRAD(zeta), i.e., the driving force, when water depth (and flow velocity) become very small  small layer of water remains. This can be obtained by adding to rhs something like g*h*GRAD(z_b)*(eps_h/(h+eps_h))^p or g*h*GRAD(z_b)*exp((-h/eps_h)^p), with eps_h dry-bed threshold and p some power. Also required: change bed-friction term -q*|q|/(C^2*h) to something like -q*(q^p+eps_q^p)^(1/p)/(C^2*h), with p even, which at the same time regularizes this term.

## Slide 21: Summarizing …
Properties of space discretization:
Smoothing errors dominant, discretization errors negligible  numerical errors can be interpreted physically!  numerical errors can be compared to physical errors!
Pretty accurate
Continuous and smooth
  very fast solvers
  robust model
(block-)Structured grids required
  flexibility by means of DD and IBM
Time integration:
To be investigated

## Slide 22: Motto
SUPPRESS THE WIGGLES, BUT SUCH THAT
THEY KEEP TELLING YOU SOMETHING!
(variation on Gresho & Lee, “Don’t suppress the wiggles—They’re telling you something!”, Comput. Fluids 1981)
Notes: Gresho & Lee, 1981: “It is further argued that it is usually an inappropriate response to develop methods which a priori suppress these wiggles and thereby make claims that these unconventional FEM techniques (MB: or any other wiggle-suppressing technique, for that matter) are actually improvements and can be used to solve difficult problems on coarse meshes.”

## Slide 23: Remarks, discussion, questions?

## Slide 25: 1D shallow-water equations
Constant channel width :
: depth
: depth-integrated velocity ( average velocity )
25

## Slide 26: Sub-/supercritical steady flow over a weir
100 finite volumes, non-smooth geometry
100 finite volumes, smoothed geometry
Notes: Number of iterations & comput.time in 2002 to reach both 10^-11 water-level conv.error and 10^-13 velocity conv.error
025FV, non-smooth/smoothed geom.: 32 & 0.06sec/30 & 0.05sec
050FV, non-smooth/smoothed geom.: 31 & 0.05sec/31 & 0.05sec
100FV, non-smooth/smoothed geom.: 39 & 0.11sec/39 & 0.11sec
200FV, non-smooth/smoothed geom.: 65 & 0.28sec/66 & 0.22sec
400FV, non-smooth/smoothed geom.: 78 & 0.61sec/78 & 0.55sec

## Slide 27: Sub-/supercritical steady flow over a weir
100 finite volumes, error on non-smooth and smoothed geometry
Notes: Number of iterations & comput.time in 2002 to reach both 10^-11 water-level conv.error and 10^-13 velocity conv.error
025FV, non-smooth/smoothed geom.: 32 & 0.06sec/30 & 0.05sec
050FV, non-smooth/smoothed geom.: 31 & 0.05sec/31 & 0.05sec
100FV, non-smooth/smoothed geom.: 39 & 0.11sec/39 & 0.11sec
200FV, non-smooth/smoothed geom.: 65 & 0.28sec/66 & 0.22sec
400FV, non-smooth/smoothed geom.: 78 & 0.61sec/78 & 0.55sec

## Slide 28: Performance of several space discretizations
Transport of wavy signal
initial solution
final solution

## Slide 29: Performance of several space discretizations
160 finite volumes (Δx=0.00625)
80 finite volumes (Δx=0.0125)
40 finite volumes (Δx=0.025)
20 finite volumes (Δx=0.05)
Transport of wavy signal, initial solution

## Slide 30: Performance of several space discretizations
Transport of wavy signal, final solution
640 finite volumes (Δx=0.0015625)
320 finite volumes (Δx=0.003125)
160 finite volumes (Δx=0.00625)
80 finite volumes (Δx=0.0125)
40 finite volumes (Δx=0.025)
20 finite volumes (Δx=0.05)

## Slide 31: Performance of several space discretizations
Transport of block with cosine slopes
initial solution
final solution

## Slide 32: Performance of several space discretizations
160 finite volumes (Δx=0.00625)
80 finite volumes (Δx=0.0125)
40 finite volumes (Δx=0.025)
20 finite volumes (Δx=0.05)
Transport of block with cosine slopes, initial solution

## Slide 33: Performance of several space discretizations
Transport of block with cosine slopes, final solution
640 finite volumes (Δx=0.0015625)
320 finite volumes (Δx=0.003125)
160 finite volumes (Δx=0.00625)
80 finite volumes (Δx=0.0125)
40 finite volumes (Δx=0.025)
20 finite volumes (Δx=0.05)

## Slide 34: Fourier-mode decompositions
Wavy signal
Block with cosine slopes

## Slide 35: Solution method
Fully implicit time integration (for steady state set and )
Newton linearization
Stabilization/regularization
Notes: Advantage of delta form: assuming convergence, process will converge to correct solution (determined by vanishing rhs) regardless of convergence process, i.e., regardless of whatever approximations and tricks are applied in lhs (“separate the numerics from the physics”). In particular, the pseudo-time step mass matrix M_pseu can be used to introduce (stabilizing?) Du upwind and/or (stabilizing?) Du smoothing in pseudo time and/or any other measure that improves convergence speed and/or robustness/stability.
Another advantage of delta form: less sensitive to round-off errors.
Best initialization of convergence process per steady state is u^{m=0} = 0 and zeta^{m=0} = constant and large enough, i.e., still-water flow in a fully filled model. This is a solution that is guaranteed to satisfy the discrete equations inside the domain, i.e., is guaranteed to be sufficiently smooth. To maintain this, do NOT apply the boundary conditions at once, but turn them on slowly, preferably by using convergence-error-dependent underrelaxation that turns itself off automatically upon reaching convergence (this is how it is done in SUPSUB).
Simplest initialization of convergence process per time step is u^n,0 = u^n-1. However, much better is to initialize this process by some estimation of u^n based on, e.g., some extrapolation in time or obtained from application of some explicit time integration scheme, e.g., leapfrog (not yet in SUPSUB).
Criterion for meaningful Newton linearization: requires sufficiently smooth L(u)!!!
Optimization of approximation of Jacobian as well as optimization of Dt_pseu required.
NB, space-varying 1/Dtvec_pseu per iteration. It is generally very advantageous to use a (locally optimized) Dt_pseu that varies in space and over the iterations.

## Slide 36: What’s next
SUPSUB next version:
embed as single-pipe component in WANDA?
better initialization per time step (unsteady applications)  increase of robustness and efficiency
better pseudo time-step scaling (based on residual and full linearization error)  increase of robustness and efficiency
proper geometry smoothing (boundary/initial condition smoothing p.m.)  some increase of accuracy, robustness, efficiency
moving error-minimizing grid adaptation (p.m.)  large increase of accuracy, efficiency, complexity
Wave modeling (Boussinesq-type, multi-layer, GABCs):
extension to 2DV, IMEX time integration?
2DH/3D with DD and IBM for modeling flexibility (p.m.)
Notes: Increase of robustness  increase of general applicability
* include missing functionality/features (geometry types, friction formulations, 2-phase flow?)
* embed as single-pipe component in WANDA (computational model for pipe networks)

## Slide 37: A wave modeling example
Port of Molfetta, Italy
25 m
10 m
11 m
8 m
Notes: port extension scale-model project (90-ies), plans never finalised/constructed
wave spectrum (Tp = 6.9 s, Hs = 2.3 m)
dir spreading
bound (‘setdown’) and free LF waves
limited spurious free waves expected
locations relevant for vessels (depth >= 8 m)